SECTION 09706

CHEMICAL RESISTANT NOVOLAC-EPOXY COMPOSITION FLOORING

Dex-O-Tex Chem-Rez “N”

Dex-O-Tex S-C Membrane

PART 1.00 - GENERAL

1.01	GENERAL REQUIREMENTS

A.	Work of this Section, as shown or specified, shall be in accordance with the requirements of the Contract Documents.

1.02	WORK INCLUDED

A.	Work of this Section includes all labor, materials, equipment and services necessary to complete chemical resistant Novolac-epoxy containment system incorporating flexibilized epoxy membrane and integral base as selected on drawings and/or specified herein.

1.03	RELATED WORK

A.	Concrete - Section 03300 (Note to Specifier:  Concrete should be either water cured or cured using sodium silicate curing compounds only.  Other types of curing compounds are generally not acceptable.  Concrete should be cured for a minimum of 28 days.  On grade floors should have functioning vapor retarder beneath slab.)

B.	Floor drains - Division 15.  (Note to Specifier:  Floor drains, clean-outs etc. should be of the “floor-flange” type as manufactured for use with composition floors by most major drain manufacturers.)

1.04   SUBMITTALS

A.	General:  Submit the following in accordance with Conditions of Contract and Division 1 Specification Sections.

B.	Product Data:  Submit manufacturer's technical data, application instructions and general recommendations for the chemical resistant Novolac-epoxy composition flooring specified herein.

C.	Chemical Resistance:  Submit manufacturer’s printed chemical resistance tables indicating that Novolac-epoxy flooring specified herein resist total immersion of cube samples in damaging reagents for a minimum of ninety (90) days testing.  Reagents shall include but not necessarily be limited to:

50% (concentrated) Sulfuric Acid		Concentrated Hydrochloric Acid

25% Acetic Acid				50% Phosphoric Acid

1, 1, 1 Trichloroethane			Acetone

Methanol (Methyl Alcohol)		Concentrated Ammonium Hydroxide

50% Sodium Hydroxide

Totally immersed samples shall show no swelling, softening, loss of adhesion, discoloration or deterioration.

D.	LEED Submittals:

1.  	Product Data for Credit MR 4.1 and Credit MR 4.2:  For products having recycled content, submit documentation indicating percentages by weight of postconsumer and preconsumer recycled content.

a.   	Include statement indicating costs for each product having recycled content.

b.	Include LEED Product Information Form for LEED Credits MR 4.1 and 4.2.

2.	Product Data for Credit EQ 4.2:  For field applied, interior, paints coatings and primers, include printed statement of VOC content indicating compliance with Credit requirements.

a.	Include LEED Product Information Form for LEED Credit EQ 4.2.

3.	Provide additional documentation for products as required to achieve each Credit(s).

E.	Samples for initial selection purposes in form of manufacturer's color charts showing full range of colors available.

1.  Submit 2-1/2" x 4" samples in color as selected.

F.	Material certificates signed by manufacturer certifying that the chemical resistant Novolac-epoxy composition flooring complies with requirements specified herein.

G.	Maintenance Instructions:  Submit manufacturer's written instructions for recommended maintenance practices.

1.05	QUALITY ASSURANCE

A.	Installer Qualifications:  Engage an experienced installer or applicator who has specialized in installing resinous flooring types similar to that required for this Project and who is acceptable to manufacturer of primary materials.

B.	Single-Source Responsibility:  Obtain chemical resistant Novolac-epoxy containment system materials including primers, resins, hardening agents and finish or sealing coats, from a single manufacturer.

1.06	DELIVERY STORAGE AND HANDLING

A.	Deliver materials in original packages and containers with seals unbroken and bearing manufacturer's labels containing brand name and directions for storage and mixing with other components.

B.	Store materials to comply with manufacturer's directions to prevent deterioration from moisture, heat, cold, direct sunlight, or other detrimental effects.

1.07	PROJECT CONDITIONS

A.	Environmental Conditions:  Comply with epoxy resin composition flooring manufacturer's directions for maintenance of ambient and substrate temperature, moisture, humidity, ventilation, and other conditions required to execute and protect work.

B.	Lighting:  Permanent lighting will be in place and working before installing flooring.

PART 2:00 - PRODUCTS

2.01	MATERIALS

A.	Chemical resistant Novolac-epoxy composition flooring shall be Dex-O-Tex Chem-Rez N (Dex-O-Tex Posi-Tred “CR” top finish) together with flexible epoxy Dex-O-Tex SC Membrane as manufactured by Crossfield Products Corp. in Rancho Dominguez, California and Roselle Park, New Jersey.

2.02	PROPERTIES

A.	Colors:  As indicated, or if not otherwise indicated, as selected by Architect from manufacturer's standard colors.

B.	Physical Properties:  Provide containment system that meets or exceeds the listed minimum physical property requirements when tested according to the referenced standard test method in parentheses.

Membrane:

Tensile Strength (ASTM D638)	1,500 psi

Tensile Modulus (ASTM D638)	17,150 psi

Tensile Elongation (ASTM D638)	96%

Tear Strength (ASTM D1938)	120 lb./in.

# Chemical Resistant Floor Finish:

Chemical Resistance	90 day - no swelling, softening, deterioration or discoloration (Note to Specifier:  List chemicals expected to be spilled on floor)

Compressive Strength (ASTM D695)	8,740 psi.

Temperature Resistance	No measurable softening, deflection or integrity loss upon 8 hours immersion in boiling water (2120F) and boiling cooking oil (>3000F)

Surface Hardness (ASTM D2240)	Durometer “D” 80-85

Tensile Strength (ASTM D638)	4,150 psi

Flexural Strength (ASTM D638)	8,370 psi.

Bond Strength 	>400psi.

(ACI Committee 503.1-92)	100% failure of concrete

Impact Resistance	Direct 50 in. lbs.

(ASTM D2794)	Reverse 15 in. lbs.

Water Absorption (MIL-PRF-3134)	NIL (7 day immersion)

2.03	SUPPLEMENTAL MATERIALS

A.	Anti-Microbial Additive:  Incorporate anti-mocrobial chemical additive to prevent the growth of most bacteria, fungi, algae and actinomycetes.  (Note to Specifier: The use of anti-microbial additive is optional.  Its use poses no health hazards.

PART 3.00 - EXECUTION

3.01	INSPECTION

A.	Examine the areas and conditions where chemical resistant Novolac-epoxy containment system is to be installed and notify the Architect of conditions detrimental to the proper and timely completion of the work.  Do not proceed with the work until unsatisfactory conditions have been corrected by the Contractor in a manner acceptable to the Architect.

3.02	PREPARATION

A.	Substrate:  Perform preparation and cleaning procedures according to flooring manufacturer's instructions for particular substrate conditions involved and as specified.  Provide clean, dry and neutral substrate for flooring application.

B.	Concrete Surfaces:  Shot-blast, acid etch or power scarify as required to obtain optimum bond of flooring to concrete.  Remove sufficient material to provide a sound surface, free of laitance, glaze, efflorescence, and any bond-inhibiting curing compounds or form release agents. Remove grease, oil, and other penetrating contaminates.  Repair damaged and deteriorated concrete to acceptable condition.  Leave surface free of dust, dirt, laitance and efflorescence.

C.	Materials:  Mix epoxy resin hardeners and aggregates when required, and prepare materials according to flooring system manufacturer's instructions.

3.03	APPLICATION

A.	General:  Apply each component of chemical resistant Novolac-epoxy composition flooring system according to manufacturer's directions to produce a uniform monolithic flooring surface of thickness indicated.

B.	Bond Coat:  Apply bond coat over prepared substrate at manufacturer's recommended spreading rate.

C.	Membrane: Apply flexibilized chemical resistant epoxy membrane to a dry film thickness of 40 mils, allow to cure.  Apply to base at height of 6” or as shown on plans.

D.	Chemical Resistant Floor Finish: Over membrane, trowel apply basecoat to nominal 3/16” thickness; hand or power trowel.  When cured, sand or grind if necessary to remove trowel marks and roughness.

E.	Finish or Sealing Coats:  After body coat has cured sufficiently, apply grout and finish coats of type recommended by flooring manufacturer to produce finish matching approved sample and in number of coats and spreading rates recommended by manufacturer for specific containment purposes.

1.   Final finish coat shall be in color and skid retardant profile as approved by the Architect.

2.   Finished floor shall be 1/4" thick uniform in color and free of trowel marks.

F.	Cove Base:  Apply cove base mix to wall surfaces at locations shown to form cove base height of 6 inches unless otherwise indicated.  Follow manufacturer's printed instructions and details including taping, mixing, priming, troweling, sanding and top-coating of cove base.

3.04	CURING PROTECTION AND CLEANING

A.	Cure Chemical resistant Novolac-epoxy containment system materials according to manufacturer's directions taking care to prevent contamination during application stages or premature chemical spillage before completing curing process.  Close application area for a minimum of 24 hours.

END OF SECTION

DEX-O-TEX PRODUCT LINE			3000 E. Harcourt Street		140 Valley Road

Crossfield Products Corp.			Rancho Dominguez, CA 90221		Roselle Park, NJ 07204

www.dexotex.com				Tel: (310) 886-9100			Tel: (908) 245-2800

Fax: (310) 886-9119			Fax: (908) 245-2583