SECTION 09820

POLYMER MODIFIED DECORATIVE THIN STAMPED

# OVERLAYMENT SYSTEM

Dex-O-Tex STAMPCOTE

PART 1.00 - GENERAL

1.01	GENERAL REQUIREMENTS

A.	Work of this Section, as shown or specified, shall be in accordance with the requirements of the Contract Documents.

1.02	WORK INCLUDED

A.	Work of this Section includes all labor, materials, equipment and services necessary to complete the polymer modified decorative thin stamped overlayment system as scheduled on the drawings and/or specified herein.

1.03	RELATED WORK

A.	Concrete - Section 03300.

(Note to Specifier:  Concrete should be either water cured or cured using sodium silicate curing compounds only.  Other types of curing compounds are generally not acceptable.  Concrete should be cured for a minimum of 28 days.)

B.	Floor drains - Division 15.

(Note to Specifier:  Floor drains, clean-outs, etc. should be of the "floor-flange" type as manufactured for use with composition floors by most major drain manufacturers.)

1.04	SUBMITTALS

A.	General:   Submit the following in accordance with Conditions of Contract and Division 1 Specification Sections.

B.	Product Data: Submit manufacturer’s technical data, application instructions and general recommendations for waterproof flooring.

C.	LEED Submittals:

1.  	Product Data for Credit MR 4.1 and Credit MR 4.2:  For products having recycled content, submit documentation indicating percentages by weight of postconsumer and preconsumer recycled content.

a.   	Include statement indicating costs for each product having recycled content.

b.	Include LEED Product Information Form for LEED Credits MR 4.1 and 4.2.

2.	Product Data for Credit EQ 4.2:  For field applied, interior, paints coatings and primers, include printed statement of VOC content indicating compliance with Credit requirements.

a.	Include LEED Product Information Form for LEED Credit EQ 4.2.

3.	Provide additional documentation for products as required to achieve each Credit(s).

D.	Samples:

1.   Submit 2-1/2” x 4” samples of underlayment as designed by the Architect.

E.	Material certificates signed by manufacturer certifying that the polymer modified decorative thin stamped overlayment system comply with requirement specified herein.

1.05	QUALITY ASSURANCE

A.	Installer Qualifications: Engage an experienced installer or applicator who has specialized in installing resinous polymer modified overlayment systems similar to that required for this Project and who is acceptable to manufacturer of primary materials.

B.	Single-Source Responsibility: Obtain polymer modified decorative thin stamped overlayment system materials from a single manufacturer.

C.	Qualified Materials: Request for material approvals for any products other than the specified product must be submitted to the architect two weeks prior to the bid, including complete application specification and physical characteristics. Any request after this date will not be accepted. Failure of performance requires immediate removal and replacement of unapproved substituted material with those originally specified at no cost to the owner, Architect, construction manager, or general contractor.

1.06	DELIVERY, STORAGE AND HANDLING

A.	Deliver materials in original packages and containers with seals unbroken and bearing manufacturer's labels containing brand name and directions for storage and mixing with other components.

B.	Store materials to comply with manufacturer's directions to prevent deterioration from moisture, heat, cold, direct sunlight, or other detrimental effects.

1.07	PROJECT CONDITIONS

A.	Environmental Conditions: Comply with polymer modified decorative thin stamped overlayment system manufacturer's directions for maintenance of ambient and substrate temperature, moisture, humidity, ventilation, and other conditions required to execute and protect Work.

B.	Lighting: Permanent lighting will be in place and working before installing resinous polyacrylate.

PART 2.00 - PRODUCTS

2.01	MATERIALS

A.	Trowel, spray or screed applied polymer modified decorative thin stamped overlayment system shall be Dex-O-Tex STAMPCOTE as manufactured by Crossfield Products Corp. in Rancho Dominguez, California and Roselle Park, New Jersey.

2.02	PROPERTIES

A.	Physical Properties:

Provide polymer modified overlayment system that meets or exceeds the listed minimum physical property requirements when tested according to the referenced standard test method in parentheses.

Compressive Strength (ASTM C109)  	4,219 psi.

Indentation Characteristics (Steadily Applied Load)	2.26%

MIL-PRF-3134, Para. 4.7.4.2.1. (2,000 lbs. on 1” steel

ram imposed for 30 mins.)

Adhesion (MIL-PRF-3134, Para. 4.7.14)	305 p.s.i.

(Shear from Steel plate after 96 hours)

Water Absorption (MIL-PRF-3134)	3.41%

Tensile Strength (ASTM C190)	925 p.s.i

Flexural Strength (ASTM C580)	2,415 psi.

Impact Resistance (Gardner Impact Tester)	No chipping, cracking, or delamination and     not more than 0.014" indentation

PART 3.00 - EXECUTION

3.01 	INSPECTION

A.	Examine the areas and conditions where the polymer modified decorative thin stamped overlayment system is to be installed and notify the Architect of conditions detrimental to the proper and timely completion of the work.  Do not proceed with the work until unsatisfactory conditions have been corrected by the Contractor in a manner acceptable to the Architect.

3.02	PREPARATION

A.	Substrate:  Perform preparation and cleaning procedures according to polyacrylate manufacturer's instructions for particular substrate conditions involved, and as specified.  Provide clean, dry, and neutral substrate for polyacrylate underlayment application.

B.	Concrete Surfaces: Shot-blast, acid etch or power scarify as required to obtain optimum bond of polyacrylate to concrete.  Remove sufficient material to provide a sound surface free of laitance, glaze, efflorescence, and any bond-inhibiting curing compounds or form release agents.  Remove grease, oil, and other penetrating contaminates.  Remove damaged and deteriorated concrete.  Leave surface free of dust, dirt, laitance, and efflorescence.

C.	Materials:  Mix resin catalyst and aggregate when required, and prepare materials according to polyacrylate underlayment system manufacturer's instructions.

3.03	APPLICATION

A.	General:  Apply each component of polymer modified decorative thin stamped overlayment system according to manufacturer's directions to produce a uniform monolithic surface of thickness indicated.

- Base Mortar:  Apply base mortar by screed at manufacturer’s directions and spread rate. Prime surface with wetting mix just prior to application of base mortar. Spray release agent to base mortar and stamp tool. Carefully place stamp tool over Stampcote screeded material. Tamp tool into place to create impression onto surface. Carefully remove stamp tool and allow release agent to evaporate.

- Sealer:  Apply Stampcote clear sealer after preparing the surface.

3.04	CURING, PROTECTION AND CLEANING

A.	Cure polymer modified decorative thin stamped overlayment system materials according to manufacturer's directions, taking care to prevent contamination during application stages and before completing curing process.  Close application area for a minimum of 24 hours.

# END OF SECTION

DEX-O-TEX PRODUCT LINE 			3000 E. Harcourt Street		140 Valley Road

Crossfield Products Corp.			Rancho Dominguez, CA 90221		Roselle Park, NJ 07204

www.dexotex.com				Tel: (310) 886-9100			Tel: (908) 245-2800

Fax: (310) 886-9119			Fax: (908) 245-2583